## Slide 1
IT 694
Computer Networks Fundamentals Week 2-Lecture 1

## Slide 2
What is a computer network?
A set of network elements connected together, that implement a set of
protocols for the purpose of sharing resources at the end hosts
•
Three important components:
•
Core infrastructure:
• A set of network elements connected together
Protocols:
• Needed to use the network
•
•

## Slide 3
What is a computer network?
A set of network elements connected together, that implement a set of
protocols for the purpose of sharing resources at the end hosts

## Slide 4: What’s a protocol?
Human protocols:
“what’s the time?”
“I have a question”
introductions
Network protocols:
computers (devices) rather than humans
all communication activity in Internet governed by protocols
Protocols define the format, order of messages sent and received among network entities, and actions taken on message transmission, receipt
Rules for:
… specific messages sent
… specific actions taken when message received, or other events

## Slide 5: What’s a protocol?
A human protocol and a computer network protocol:
Hi
Hi
Got the
time?
2:00
time
TCP connection
response
<file>
TCP connection
request
GET http://gaia.cs.umass.edu/kurose_ross
Notes: Explain important points
distributed entities, exchanging messages (governed by protocols)
Time going down
go over definition of protocol (showing format, order of messages sent and received, and actions taken)
We’ll see these kinds of diagrams a lot

## Slide 6
What do computer networks do?
A computer network delivers data between the end points/hosts
•
One and only one task: Delivering the data
•
This delivery is done by:
•
•
Chopping the data into packets
Sending individual packets across the network
• Reconstructing the data at the end points
Evolution of Technology, Infrastructure, protocols, and purpose

## Slide 7: A closer look at network structure:
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 8: Access networks: cable-based access
cable
modem
splitter
…
cable headend
data, TV transmitted at different
frequencies over shared cable
distribution network
HFC: hybrid fiber coax
  asymmetric: up to 40 Mbps – 1.2 Gbps downstream transmission rate, 30-100 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
cable modem
termination system
CMTS
ISP

## Slide 9: Access networks: digital subscriber line (DSL)
ISP
central office
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  24-52 Mbps dedicated downstream transmission rate
  3.5-16 Mbps dedicated upstream transmission rate
DSL
modem
splitter
DSL access
multiplexer

## Slide 10: Links: physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps Ethernet

## Slide 11: Links: physical media
Coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple frequency channels on cable
  100’s Mbps per channel
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (10’s-100’s Gbps)
low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 12: The network core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity

## Slide 13: Many mechanisms: What do we mean by …
Locating a destination? Naming, Addressing
Finding path to the destination  Routing
Sending data to the destination  Forwarding
Failures, reliability,etc.. Distributed routing and congestion control

## Slide 14
How GOOD is a NETWORK?

## Slide 15: What do we look at before commuting to places?
Which are the possible routes to take from DAIICT to home?
Which one is the best?
How long does it take to reach my home from DAIICT?
What is the capacity of a road(s) between DAIICT and home?

## Slide 16: Capacity
How wide is the road?
How fat is the tunnel?
How many cars can fit at a time?
  One, two, three…?

## Slide 17
Performance metrics in computer networks!
Capacity is Bandwidth: Number of bits sent per unit time (bits per second, or bps)
• Depends on
Bandwidth
• Hardware
• Network traffic conditions
Time taken is Propagation delay: Time for one bit to move through the link (seconds)
• Depends on
•
•
Hardware
Network traffic conditions
Propagation
Delay
• How large is the unit?

## Slide 18: Bandwidth
Each bit is a pulse of some width.
For example, each bit on a
  1-Mbps link is 1 µs wide
  2-Mbps link is 0.5 µs wide,
The narrower each bit can become, the higher the bandwidth.
  This means more bits can get inside the tunnel
  So MORE DATA CAN FLOW WITHIN A TIME

## Slide 19
Bandwidth-delay product (BDP)
Number of bits “in flight” at any point of time (bits)
• Bits sent, but not received
Bandwidth
Bandwidth x delay
Propagation
Delay
•
Same city over a slow link
•
Bandwidth: ~100Mbps
• propagation delay: ~0.1ms
• BDP = 10,000 bits (1.25KBytes)
Between cities over fast link:
• Bandwidth: ~10Gbps ,
propagation delay: ~10ms
• BDP = 100,000,000 bits (12.5MBytes)

## Slide 20
Who is the father of the Internet?
Vincent Cerf
Who is the father of the World Wide Web?
Tim Berners Lee

## Slide 21: Match
PC
  End
  Intermediary
Printer
  End
  Intermediary
Firewall
  End
  Intermediary
Smart Device
  End
  Intermediary
Router
  End
  Intermediary
Switch
  End
  Intermediary

## Slide 22
A person X recently got a job with a computer support services company in his hometown Gandhinagar. A customer has asked for someone to come connect their home network to the Internet. They only have a cable modem. Which of the following devices would X most likely take with him to complete the task?
wireless router
LAN switch
desktop computer
firewall appliance
wireless router

## Slide 23: Match
PC
  End
  Intermediary
Printer
  End
  Intermediary
Firewall
  End
  Intermediary
Smart Device
  End
  Intermediary
Router
  End
  Intermediary
Switch
  End
  Intermediary

## Slide 24
Source: Cisco Networking Academy